## Slide 1: Scale articulation
Prof.dr.ir. Taeke M. de Jong
Rīga Masterclass October 27th 2014

## Slide 2: The domain of Urban and Architectural design
Imagine a school with elevators and corridors leading you through different spatial levels, time-spans, and layers of design.

## Slide 3: A scale paradox, its factor 3
Any conclusion about space is scale-sensitive.
It can change into its opposite already with a factor 3 of scale.

## Slide 4: Ten levels of difference to be explored
Look for differences at any level of scale

## Slide 5: A frame 100x the grain of a drawing representing a building
Any representation has an upper and a lower boundary:
a frame and a grain.
Let us notate them as a ‘nominal radius’ R and r.

## Slide 6: Boundaries of nominal R and r
A ‘nominal’ radius is a name for a range of measures.
‘R=10m’ is something between 3m and 30m.

## Slide 7: Usual names fitting R=

## Slide 8: Object in Context (months, years)
Any object has impacts in different layers of context at different levels of scale.
A programme is simply a set of intended impacts.

## Slide 9: Ten levels of difference to be explored
Look for differences at any level of scale

## Slide 10: Content diversifies space
Some values of named variables may serve as legend units.

## Slide 11: Form distributes content in space

## Slide 12: Form = state of distribution
Accumulation
Deconcentration
Concentration
Sprawl

## Slide 13: States of distribution of 100 dots
Any shape appears between total sprawl and total accumu-lation

## Slide 14: Concentration and Deconcentration at 2 levels ...
… result in accumulation and sprawl at different levels of scale.

## Slide 15: Structure stabilises form

## Slide 16: Functions at different levels of scale

## Slide 17: Intentions about the object in its context
Stakeholders, specialists and users can be located on scale and layer.
Ask them to specify the intentions and expectations in their position.

## Slide 18: Intentions and expectations are different modes of thinking

## Slide 19: What is spatial quality?

## Slide 20: Quality as a function of variety

## Slide 21: Variety in modes, orders, levels and layers
modes | orders | levels | layers
probable | intention | … | managerial
possible | function | 1mm | cultural
imaginable | structure | … | economic
 | form | 1m | technical
desirable | content | 3m | biological
 |  | 10m | physical
 |  | … | 

## Slide 22: Further reading
€5,-

## Slide 23: Exercise 1: R=100m ensemble form
Prof.dr.ir. Taeke M. de Jong
Rīga Masterclass October 28th 2014

## Slide 24: Mirroring the smallest urban island
76% public pavement
67% public pavement
30x30m
30x60m W-E mirroring
Notes: Fig. 19 grid measure of 30x30m.
excessive surface of public pavement (here 76%!),
leaving relatively little for sale (here maximally 22%) paying for that public space.
Fig. 20 30x60m W-E mirroring
W-E mirroring elongates the urban island reducing public pavement (here into 67%).
The gained surface: a green margin of 9m drawn East and 2.50m drawn South:
one side with parking places is enough to reach more than 1 parking place per dwelling.
The shadow of the N side is best suitable for parking.
W and E roads are used for entrance to houses at both sides and back gardens get more privacy.
The lots for sale differentiate in morning~ and evening sun lovers.

## Slide 25: Taking sun into account
65% public pavement
66% public pavement
60x30m N-S Turning and repeting
60x30m N-S mirroring
Notes: Fig. 21 60x30m N-S Turning and multiplying
South gardens.
short sides used for parking, forcing cross-parking to reach >1 parking places per dwelling.
The path round the back enlarged at the expense of sidewalks to give proper front access to the Southern block.
Fig. 22 60x30m N-S mirroring
North gardens, drawn longer here to get a partly sunny view on the N garden still.
It differentiates the lots for sale in size
suggests a different dwelling type for sun lovers with south gardens and
artistic life style with Northern light rooms such as studios.

## Slide 26: Elongating
66% public pavement
52% public pavement
60x30m elongating
60x60m mirroring
Notes: Fig. 23 60x30m elongating
one sided elongating avoids the path round the back utilizing the side walk, giving back a proper size to the sidewalks N and S.
East gardens are suitable for people who prefer morning sun in the garden and in the sleeping room.
Pavement is still 66%.
Fig. 24 60x60m mirroring
Mirroring gives evening people a chance
both gardens more privacy.
It differentiates use and plantation.
The enlargement of the urban island again reduces the amount of pavement, now into 52%
in favour of the margins possibly used as green area: 9m East and 5m South.

## Slide 27: L-shape and U-shape
66% public pavement
52% public pavement
60x30m L-shape
60x60m U-shape
Notes: Fig. 25 60x30m L-shape
perpendicular blocks provide streetcorners with front entrances in 2 directions.
urban look and safety by private control of public space on both roads involved.
design solutions for corners, not implemented here
struggle with smaller or no gardens in the corner.
Fig. 26 60x60m U-shape
U-shaped allotments with one open side, here avoiding North gardens.
reducing pavement from 66% into 52%
green margins of 9m East and 5m South.
S gardens go 0.5m around the back now, giving space for ivy-covered side façades avoiding grafitti.

## Slide 28: Closed urban islands
46% public pavement
44% public pavement
90x60m Closing
100x60m Elongating and adapting
Notes: Fig. 27 90x60m Closing
a usual allotment type of 90m length, leaving a 9m green margin East to fill the urban grid of multiples by 30m.
Limiting parking places to N and S urges cross parking
little space for sidewalks.
Fig. 28 Elongating and adapting 100x60m
elongating to 100m is easy by adding 2 houses West and East.
shortage of parking places then forces parking at all sides.
giving up cross parking N and S, there is space for 6 extra houses in total.
The reduction of pavement is 2% only, but the number of parking places is 1.4 per dwelling.
the green margin is distributed W and E to make trees possible.

## Slide 29: A neighbourhood
Notes: multiply the module (M 100x60m) 5 times E-W and 3 times N-S
reach the mesh width (300mx300m) for neighbourhood roads (30m width of pavement).
15 modules together surrounded by larger neighbourhood roads requiring extra space.
These ‘neighbourhood islands’ we call ‘neighbourhood quarters’, because 4 of them make a neighbourhood.

## Slide 30: A 3D simulation…

## Slide 31: … may generate new ideas

## Slide 32: Exercise 1, R=100m ensemble form

## Slide 33: Exercise 2: R=300m neighbourhood form
Prof.dr.ir. Taeke M. de Jong
Rīga Masterclass October 28th 2014

## Slide 34: Exercise 2, R=300m neighbourhood form
Redistribute 44 dots of 100 inhabitants (r1=30mfloor+3mparking).
Replace one dot r1 as neighbourhood centre.
Any dot r1=30m can be split up into 10 dots of 10 inhabitants (r2=10m).
Add a neighbourhood park r3=100m.
Widen 5 residential roads (5 x 600m long and 6m width) into neighbourhood roads (12m width).

## Slide 35: Standard Green Structure
Within any radius R an average distance r=R/3 into a substantial (1/10) green area.

## Slide 36: Primary profile spaces needed
Pedestrian 50 + 2 x 5  60 cm | Cyclist 75 + 2 x 15  100 cm | Car 30 km/h 200 + 2 x 15  230 cm | Bus 50 km/h 255 +2 x 25 300 cm

## Slide 37: A neighbourhood

## Slide 38: Nes; Zijpp (2000) Scale Factor 3 For Hierarchical Road Networks A Natural Phenomenon? (Delft)Trail

## Slide 39: A factor 3 network hierarchy
Category |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
 |  | residential path | residential street | neighbourhood road | district road | urban highway | highway | regional highway | metropolitan highway
 | served area | estate | ensemble | neigh-bourhood | district | town | conur-bation | region | metropoli-tan region
m radius ¦ mesh ¦ crossing distance |  | 30 | 100 | 300 | 1 000 | 3 000 | 10 000 | 30 000 | 30 000
served inhabitants |  | 10 | 100 | 1 000 | 10 000 | 100 000 | 1 mln | 10 mln | 100 mln
number of floors |  | 1 | 2 | 3 | 4 | 6 | 7 | 8 | 10

## Slide 40: Excel profile generator

## Slide 41: 1 Standard residential path 10m

## Slide 42: 2 Standard residential street 20m

## Slide 43: 3 Standard neighbourhood road 30m

## Slide 44: 4 Standard district road 40m

## Slide 45: 5 Standard urban highway 60m

## Slide 46: 6 Standard highway 70m

## Slide 47: 7 Standard regional highway 80m

## Slide 48: 8 Standard metropolitan highway 100m

## Slide 49: Physical measures, capacity and residential intensity
Category | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
Physical infrastructure |  |  |  |  |  |  |  | 
m width between facades | 10 | 20 | 30 | 40 | 60 | 70 | 80 | 100
km/hour design velocity | 10 | 30 | 50 | 70 | 90 | 110 | 130 | 150
m minimum lane width | 1,75 | 2,25 | 2,75 | 3,25 | 3,25 | 3,25 | 3,25 | 3,25
number of lanes | 1 | 2 | 2 | 2 | 4 | 8 | 10 | 16
Capacity (possible use) |  |  |  |  |  |  |  | 
vehicles/h capacity per lane | 500 | 1 000 | 1 500 | 2 000 | 2 000 | 2 000 | 2 000 | 2 000
vehicles/hour capacity | 500 | 2 000 | 3 000 | 4 000 | 8 000 | 16 000 | 20 000 | 32 000
vehicles/24 hour capacity | 5 000 | 20 000 | 30 000 | 40 000 | 80 000 | 160 000 | 200 000 | 320 000
Use ¦ Intensity |  |  |  |  |  |  |  | 
residential |  |  |  |  |  |  |  | 
directly served inhabitants | 10 | 100 | 1 000 | 10 000 | 100 000 | 1 mln | 3 mln | 10mln
car rides/inhabitant/day | 2,00 | 2,00 | 2,00 | 1,00 | 0,20 | 0,10 | 0,05 | 0,02
%surrounding infrastructure used | 50% | 50% | 50% | 50% | 50% | 50% | 50% | 50%
light vehicles/24 hour intensity | 20 | 200 | 2 000 | 10 000 | 20 000 | 100 000 | 150 000 | 200 000

## Slide 50: Adding cargo and service, noise
Category | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8
cargo |  |  |  |  |  |  |  | 
kg cargo/inhabitant per day | 1,00 | 1,00 | 1,00 | 1,00 | 1,00 | 1,00 | 1,00 | 1,00
kg cargo/vehicle | 10 | 100 | 1 000 | 1 000 | 1 000 | 1 000 | 1 000 | 1 000
cargo vehicles/24 hour intensity | 2 | 2 | 2 | 20 | 200 | 2 000 | 6 000 | 20 000
service |  |  |  |  |  |  |  | 
service visit/inhabitant/day | 0,01 | 0,01 | 0,01 | 0,02 | 0,01 | 0,00 | 0,00 | 0,00
service vehicles/24 hour intensity | 0,20 | 2,00 | 20 | 400 | 2 000 | 2 000 | 6 000 | 2 000
Total including residential use |  |  |  |  |  |  |  | 
vehicles/24 hour intensity | 22 | 204 | 2 022 | 10 420 | 22 200 | 104 000 | 162 000 | 240 000
vehicles/hour intensity | 2 | 20 | 202 | 1 042 | 2 220 | 10 400 | 16 200 | 24 000
vehicles/hour peak intensity |  |  |  |  |  |  |  | 
% use by car = intensity/capacity | 0,4% | 1,0% | 7% | 26% | 28% | 65% | 81% | 75%
noise |  |  |  |  |  |  |  | 
dB(A) noise on façade | 66 | 59 | 62 | 74 | 80 | 84 | 90 | 96
% devaluation houseprice by noise | 10% | 5% | 7% | 22% | 34% | 40% | 48% | 54%

## Slide 51: Exercise 2, R=300m neighbourhood form
Redistribute 44 dots of 100 inhabitants (r1=30mfloor+3mparking).
Replace one dot r1 as neighbourhood centre.
Any dot r1=30m can be split up into 10 dots of 10 inhabitants (r2=10m).
Add a neighbourhood park r3=100m.
Widen 5 residential roads (5 x 600m long and 6m width) into neighbourhood roads (12m width).

## Slide 52: Exercise 3: R=1km district
Prof.dr.ir. Taeke M. de Jong
Rīga Masterclass October 28th 2014

## Slide 53: Exercise 3, R=1km district
Redraw a next component of R=1km (70 000inh.), r1=30m (100inh.), r2=100m green, r3=300m green

## Slide 54: Look for components and details

## Slide 55: Cerda and Buchanan
Plan Cerdà (1867) in Barcelona
A Cerdà neighbourhood
The Buchanan grid put in a square 2x2km
Residential streets 20m
Neighbourhood roads 30m
District roads 50m wide
Cut-off corners make a square of every crossing
Square neighbour-hoods
Hexagonal neighbourhoods: less pavement and traffic calming

## Slide 56: The formation of rectangles
Elongating diminishes the number of crossings
Length (L) and width (W) of the mesh for the same net density of
2 km/km2
A higher order straightens a hexagonal pattern

## Slide 57: The advantage of rectangularity (Bach)
Making a short cut as long as the detour
Easily providing a centre
Easily diminishing access crossings
Easily introducing one way traffic
Easily giving way to other networks such as cycle paths
Exceptions draw special attention
Easily accepting ongoing green lines
Easy hinging to other grids
Crooked grids keep easy orientation
However, he content of a crooked grid is less than a rectangular one, while its outline is the same as the square.
So, it will cost more pavement per inhabitant.

## Slide 58: Safe residential paths save pavement

## Slide 59: Less roads Central space looks larger
Same built-up area optically full or empty
Leaving out some neigbourhood roads

## Slide 60: T-crossings safer than X-crossings (Camillo Sitte)
A roundabout: 4 T-crossings

## Slide 61: Zoetermeer’s T-crossing strategy
A nice idea, but the drivers appear to take equal risk:
they drive faster.
First sketch
Realized

## Slide 62: Tunnels: slopes divide adjacent neighbourhoods

## Slide 63: Count your crossings (costs)
 | residential streets (20m wide) | neighbourhood roads (30m wide) | district roads (40m wide)
residential streets | 32 |  | 
neighbourhood roads | 20 | 4 | 
district roads | 4 | 2 | 1
main ditches (3m wide) | 16 | 8 | 4
water courses (10m wide) |  | 5 | 2

## Slide 64: Dry networks

## Slide 65: Wet networks

## Slide 66: Interference of dry and wet networks
Elongating saves crossings

## Slide 67: Superposition and interference
Rivers, canals and brooks
Superposition of races
Interference with highways
Interference with highways and railways

## Slide 68: Pedestrians
Reichow: car first
Runcorn: pedestrian first

## Slide 69: Public transport(Bach)
Collecting travellers
Connecting travellers

## Slide 70: Types of bus stops
Island type of central bus station
Herringbone type of central bus station

## Slide 71: Two types of shopping centres with a bus stop

## Slide 72: Exercise 3, R=1km district
Redraw the next component of R=1km (70 000inh.), r1=30m (100inh.), r2=100m green, r3=300m green

## Slide 73: Exercise 4: R=3km town, city
Prof.dr.ir. Taeke M. de Jong
Rīga Masterclass October 28th 2014

## Slide 74: Exercise 4, R=3km town, city
Characterise the components of the city with a name explaining their identity.
Draw dots of standardised size (r={100m, 300m}) for non-residential functions.

## Slide 75: Variables, legend units, character

## Slide 76: Social and urban specialisation to be recognisable in towns
 | Specialisation | Urban facilities
Administration | legislative power | town hall, parliament
 | legal/administrative | law court/government services
 | executive power | police station, prisons, military facilities
Culture | religion/ ideology | churches, monuments, signs
 | art/science | museums, institutes, libraries
 | up-bringing/education | schools
Economy | production | companies, offices
 | exchange | infrastructure, shops, banks
 | consumption | hospitals, leisure facilities, parks, dwellings

## Slide 77: Production

## Slide 78: GuiYang Masterplan of Kingsbury International Holdings 2007

## Slide 79: An alternative for sprawl
Analysis of the masterplan
Concentration

## Slide 80: Give the mountain a crown

## Slide 81: Strengthen the landscape

## Slide 82: Exercise 4, R=3km town, city
Characterise the components of the city with a name explaining their identity.
Draw dots of standardised size (r={100m, 300m}) for non-residential functions.

## Slide 83: Exercise 5: R=10km conurbation
Prof.dr.ir. Taeke M. de Jong
Rīga Masterclass October 28th 2014

## Slide 84: A dotmap adds form and surface to a list of data

## Slide 85: Easy visualizing proposals for change

## Slide 86: Exercise 5, R=10km conurbation
Make a dotmap R=10km, r=100m (1000 inhabitants) of Rīga using municipal data of inhabitants per district, and a map showing the built-up areas in order to approach the form.

## Slide 87: Exercise 6: R=30km urban region
Prof.dr.ir. Taeke M. de Jong
Rīga Masterclass October 28th 2014

## Slide 88: Exercise 6, R=30km urban region
Characterise the components of the region with a name explaining their identity.
Name variables expressing changes of character over 30km
Name some of their values as useful legend units

## Slide 89: Exercise 6, R=30km urban region
Characterise the components of the region with a name explaining their identity.
Name variables expressing changes of character over 30km
Name some of their values as useful legend units

## Slide 90: Easy making scenarios (Adapazarı)
1 000 inhabitants or employees
gross dots r1=300m (30ha)
net dots r2=100m (3ha)
Actual
400 000 inh.
High risk
2 000 000 inh.
Low risk
2 000 000 inh.

## Slide 91: Phases of sprawl R=30km, this time …

## Slide 92: … may create identity R=1km, r={300, 100m}

## Slide 93: Exercise 6, R=30km urban region
Characterise the components of the region with a name explaining their identity.
Name variables expressing changes of character over 30km
Name some of their values as useful legend units

## Slide 94: Exercise 7: R=10km Rīga conurbation
Prof.dr.ir. Taeke M. de Jong
Rīga Masterclass October 29th 2014

## Slide 95: Exercise 7, R=10km Rīga conurbation
Compare the mesh-width of roads with the hierarchy of page 29.
Indicate areas with the number of their lowest category (1-8).
Indicate missing categories.
Compare the distribution of green with the SGS of page 20.
Write a proposal for a design study about the Rīga conurbation.

## Slide 96: A not yet existent object has a scale, an existent context and desired impacts

## Slide 97: A subregional object in its regional economic context
Our project has a radius of 10km.
We do not take less than 100m into account.
The context is 30km regional economy.
We hope that the project will have a positive impact (P) in its economic context.
But, this desired impact depends on tacit expectations about the future.

## Slide 98: Next screen of the program: our expectations in the relevant fields
We expect 10km concentration (C), …
… but 100m deconcentration (D), …
… and regional economic growth (+)
If these expectations until 2030 are legitimate,
then we may hope that our project will contribute to the regional economy.

## Slide 99: A study proposal generated by the program
If you push the button left below, than an adaptable .txt concept proposal is made in the map where the program itself is located on your computer.

## Slide 100: Your concept proposal from the computer
CONTENTS
<as soon as you have added a heading style to each heading in Word, you can automatically insert a list of contents here>
1 OBJECT OF STUDY AND ITS CONTEXT
1.1 OBJECT OF MY STUDY
The object of study has the resolution of a drawing for 2030 on conurbation (R=10km) scale with smallest details on Ensemble(r=100m) level.
1.2 PROBABLE FUTURE CONTEXT: FIELD OF PROBLEMS
My assumptions about the probable future context of the object of study until 2030 are:

## Slide 101: Your probable future context
Future 2030 | Global(10000km) | Continental(3000km) | Subcontinental(1000km) | National(300km) | Subnational(100km) | Regional(30km) | Conurbation(10km) | Town(3km) | District(1km) | Neighbourhood(300m) | Ensemble(100m) | Buildingcomplex(30m) | Building(10m) | Buildingsegment(3m) | Buildingpart(1m) | Buildingcomponent(300mm) | Superelement(100mm) | Element(30mm) | Subelement(10mm) | Supermaterial(3mm) | Material(1mm) | Submaterial(<1mm) | 
management |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
culture |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
economy |  |  |  |  |  | + |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
technique |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ecology |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
physics |  |  |  |  |  |  | C |  |  |  | D |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 102: A probable but not desirable future delivers your problem statement
As far as this future is not desirable it will generate a field of problems.
As relevant probable but undesired development (emerging problems) I consider: a less attractive region if population increases without a plan accommodating economic growth.
1.3 DESIRED IMPACTS OF MY STUDY: FIELD OF AIMS
My study derives its motivation, intention, aims or even programme of requirements from fields indicated by a P in the next table:

## Slide 103: Desired impacts of your study
Impacts 2030 | Global(10000km) | Continental(3000km) | Subcontinental(1000km) | National(300km) | Subnational(100km) | Regional(30km) | Conurbation(10km) | Town(3km) | District(1km) | Neighbourhood(300m) | Ensemble(100m) | Buildingcomplex(30m) | Building(10m) | Buildingsegment(3m) | Buildingpart(1m) | Buildingcomponent(300mm) | Superelement(100mm) | Element(30mm) | Subelement(10mm) | Supermaterial(3mm) | Material(1mm) | Submaterial(<1mm) | 
management |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
culture |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
economy |  |  |  |  |  | P |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
technique |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
ecology |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
physics |  |  |  |  |  |  | O |  |  |  | o |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 104: Who may support your study?
It also indicates which actors (problem owners) will be primarily favoured by realising the results of my study:
An actor on the layer and level of growing (+) Regional(30km) economy is the economic department of the region.
It possibly will support an assignment and a programme of requirements to change undesired developments.

## Slide 105: Your design means and abilities, your proposal
1.4 MY DESIGNERLY REFERENCES: FIELD OF MEANS
Examples within a similar context below fascinate me professionally: …
1.5 MY PORTFOLIO AND PERSPECTIVE: FIELD OF ABILITIES
From my previous work, next elements are useful for this project.
2 MY STUDY PROPOSAL
2.1 LOCATION AND OTHER FUTURE CONTEXT FACTORS
The object of study has the resolution of a drawing for 2030 on Conurbation(R=10km) scale with smallest details on Ensemble(r=100m) level. The actual object will be located in Latvia.

## Slide 106: Your programme of requirements, expected results and time table
2.2 MOTIVATION OR PROGRAMME OF REQUIREMENTS
With regard to my assumptions about the future context (1.2) and referring to the intended impacts (1.3) as a result of this study
Regional(30km) economy usually growing (+) should be supported through the design of efficient economic concentrations.
2.3 INTENDED RESULTS, CONTRIBUTIONS AND PLANNING
I expect next products of my study: …
It has enough limitations to be realised in next time table: …
<add here a time table>

## Slide 107: Criteria for quality and references
3 ACCOUNTS
3.1 MEETING CRITERIA FOR A STUDY PROPOSAL
This study proposal demonstrates:
A Affinity with designing.
B University latitude.
C Concept formation and transferability.
D Retrievability and Accumulating capacity.
E Methodical accountability and depth.
F Ability to be criticised and to criticise.
G Convergence and limitation.
3.2 REFERENCES

## Slide 108: Let us ask the stakeholders, specialists and future users

## Slide 109: Exercise 7, R=10km Rīga conurbation
Compare the mesh-width of roads with the hierarchy of page 29.
Indicate areas with the number of their lowest category (1-8).
Indicate missing categories.
Compare the distribution of green with the SGS of page 20.
Write a proposal for a design study about the Rīga conurbation.

## Slide 110: Exercise 8: R=3km Rīga city
Prof.dr.ir. Taeke M. de Jong
Rīga Masterclass October 29th 2014

## Slide 111: Exercise 8, R=3km Rīga city
Re-arrange non-residential functions according to your characterisation (see page 62 and 66).
Indicate industrial areas with specialised facilities for specialised enterprises.
Indicate shopping centres on city~ and district level.

## Slide 112: Shopping malls

## Slide 113: Exercise 9: R=1km Rīga district
Prof.dr.ir. Taeke M. de Jong
Rīga Masterclass October 29th 2014

## Slide 114: Exercise 9, R=1km Rīga district
Draw a composition of neighbourhood components (see page 9).
Look for design means in order to make them recognisably different.
Look for proper locations of shopping and enterprises.
Diversify plantation per neighbourhood

## Slide 115: Plantation

## Slide 116: Exercise 10: R=0,3km Rīga neigbourhoods
Prof.dr.ir. Taeke M. de Jong
Rīga Masterclass October 29th 2014

## Slide 117: Exercise 10, R=0,3km Rīga neigbourhoods
Re-arrange these neighbourhoods adding 1000 inhabitants to the
13 000 drawn.

## Slide 118: Highrise and sun

## Slide 119: Exercise 11: R=0,1km Rīga ensemble
Prof.dr.ir. Taeke M. de Jong
Rīga Masterclass October 29th 2014

## Slide 120: Exercise 11, R=0,1km Rīga ensemble
Concentrate this ensemble into less, but higher buildings.

## Slide 121: Simulations may challenge

## Slide 122: From building into neighbourhood

## Slide 123
ÝVa10m
Va30m
Va10m
Va3m
Va1m
ÝRe10m
Re30m
Re10m
Re3m
Re1m
ÝVa10m
Va30m
Re10m
Va3m
Re1m

## Slide 124
ÝVa10m
Va30m
Re10m
Va3m
Re1m
ÝRe10m
Va30m
Re10m
Re3m
Re1m
ÝVa10m
Va30m
Re10m
Va3m
Va1m
ÝVa10m
Va30m
Va10m
Va3m
Va1m